## Slide 1: San Diego Regional Clean Cities School Bus Electrification - Lunch & Learn 1/9/25 Energetics, CLEAResult Energy Sustainability Consulting Jason Greenblatt & Kevin Wood

## Slide 2
Evaluation Year 3 (2023)
Fleet, Public& Workplace Charging Investments

## Slide 3: Pritchard Hierarchy of Electric Vehicle Charging
Make sure assets provide vehicle utilization
Then do the special stuff
Iterate, assess, implement, reassess along the way

## Slide 4: School bus (and other markets) Charging Operations AMI (utility meter data)
Typical morning peak at 10AM
  <5 hours of dwell time
Typical evening charging
  >12 hours of dwell time
  Two evening peaks
    split by use of load management

## Slide 5: Network Service Provider (Charging Session) Data
Useful to characterize “charging flexibility”
Time stamps
  Session start (plug in/out)
  Power draw (start/end)
Consumption and demand
EVSE/port

## Slide 6: Plentiful Opportunity to Save $$$ on Monthly Utility Bills
Cost and GHG analysis based on Charging Flexibility & hardware
Other utilities have aligned Super Off Peak (lowest cost times) with least emissions times
  SDG&E is in process with CPUC
Optimization prioritized Cost savings
  Following Year 4 (2024) analysis to dig into emissions optimization

## Slide 7: General Reporting Awareness
Costs by Site, installed kW, Vehicle
  See also HD, MD, Transit Bus

## Slide 8: Cajon Valley EV and V2G Pilot
Unique option to jointly bill Building & EV Charging
Several years of operations
Early generation technology (buses and chargers)
Discharging under SDG&E’s ELRP in ‘22&’23 (as reported)
6 Borg Warner – Rhombus DC chargers
Mix of bus generations
45-60kw charging
25-45 kw discharge
120-210 kWh
One data logger swapped mid project to another bus
Significant mix of DC & Level 2 Charging
L2 an indicator of DC issues
results in limiting V2G
Significant energy remaining in battery after each driving shift

## Slide 9: Bus and Building Experience and Modeling
(small for 6-chargers & buses)
365 - Daily
Limited (~50) hours of annual ELRP availability
Increase usable hours throughout year with Net Metering (>500%) and Peak Shaving (>900%)
Some opportunity to charge before On Peak
  Prepare for energy-price arbitrage from Net Metering discharge
Future V2G oriented rates on horizon

## Slide 10: Considerations
Funding options towards projects
  Rule 45, SB350, HVIP, etc.
  Easements, ownerships/site control, etc.
Power capacity and access
How can different electricity consumption needs work together?
Options re: billing tariffs, programs
  New VGI oriented tariffs from each IOU
  Continued demonstration projects (PG&E V2X and SCE Rialto USD, Large Oakland Unified Zum V2G)